EMS TDR, Entrance Matting System Tretford Design Range, Aluminium Grid Entrance Matting, low profile

TYPICAL SPECIFICATION					                                                                                                             N10 General Fixtures/Furnishings/Equipment           300 Entrance Matting         40 Miscellaneous Fittings

| Reference | EMS TDR |
| --- | --- |
| Height | 12mm |
| Insert | Tretford natural goat hair available in 48 colours |
| Installation | Recessed in matwell with 16 x 16 x 3mm frame or surface-laid with ramp frame |

DETAILED SPECIFICATION

| Reference | EMS TDR |
| --- | --- |
| Conformity | Manufactured to ISO9001:2008. Conforms to current BS8300 DDA Regulations |
| Grid Construction | Aluminium – minimum 80% recycled content in closed construction format |
| Insert | Tretford natural goat hair available in 48 colours |
| Height | 12mm |
| Module Size | EMS panels are manufactured specifically to customer requirements. Panel lengths upto 4000mm left to right as required |
| Fire Rating | Hot Metal Nut BS4790:1987 (1996) |
| Installation | Recessed in matwell with 16 x 16 x 3mm or surface-laid with ramp frame |
| Anodising Options | Aluminium grid can be anodised black, gold, grey or bronze |

Description

EMS Tretford Design Range aluminium grid entrance matting is a primary matting system for specification in commercial applications where the removal of footborne dirt is essential.  The Tretford Design Range is manufactured for medium traffic areas where design and functionality are imperative.  The Tretford is ideal in offices and hotels where corporate colours and logos can be incorporated within the system.

The matting is bespoke made.  Each front to back panel has a male and female edge which lock together.  Any left to right size can be achieved by simply butting the panels together.  No T-Bar is  required.  All EMS matting systems come with a 20 year guarantee on the alminium grid and interchangable infills.

Entrance Matting Systems                                                                                                                                                                                  Unit 12 -14 Freiston Enterprise Park, Boston, Lincolnshire PE22 0JZ

T: +44 (0) 1205 761757        F: +44 (0) 1205 761811         E: info@entrance-matting.com	                                                                W: www.entrance-matting.com